Chapter 4 Connecting Smart Objects

---
For IoT to produce data that is to be visualized, the sensors and actuators have to be connected using various protocols.
To achieve this connectivity, characteristics and communications criteria as well as The various technologies used need to be studied
The communication criteria that needs to be expounded include;
    - Range, Frequency Bands, Power Consumption, Topology, Constrained Devices, Constrained-Node Networks.
Technologies for connecting smart objects include;
    - IEEE 802.15.4, IEEE 802.15.4g and IEEE 802.15.4e, IEEE 1901.2a, IEEE 802.11ah, LoRaWAN, NB-IoT and Other LTE Variations.

---
1. Communications Criteria
In connecting things both wired and wireless connections are available or under development.
[Image from Senseware blog on iot-implementations-wireless-vs-wired]
Wireless Connections is more prevalent over wired because it eases deployment and allows smart objects to be mobile, changing location without losing connectivity. But nevertheless, wired connections are used where necessary.

---
1. Range
Range as one of the communication criteria helps us to answer the following questions while evaluating options of wired and wireless access technologies.
  - How far does the signal need to be propagated?
  - That is, what will be the area of coverage for a selected wireless technology?
  - Should indoor versus outdoor deployments be differentiated?
Short Range:
The classical wired example is a serial cable. Wireless short-range
technologies are often considered as an alternative to a serial cable, supporting tens
of meters of maximum distance between two devices. Signals are transmitted as low as 10 kbit/s making it not suitable for deployment in most cases.
Examples include Bluetooth and Visible Light Communications

---
Medium Range
- This connection spans from 10 to 100 of meters, the maximum distance is generally 1 mile (1600 meters) between two devices.
  RF technologies do not have real maximum distances defined, as long as the radio signal is transmitted and received in the scope of the applicable specification.
Medium Range Wireless Technologies
   -IEEE 802.11 Wi-Fi,
   -IEEE 802.15.4,
   -802.15.4g WPAN
Wired Technologies
  -IEEE 802.3 Ethernet
  -IEEE 1901.2 Narrowband Power Line Communications (PLC)

---
- Long range
  Two devices with distance of 1 mile between themselves require long – range technologies.
  Examples include cellular(2G, 3G and 4G and 5G) and outdoor IEEE 802.11 Wi-Fi and Low-Power Wide-Area (LPWA) technologies.
  Long range connections are found mainly in Industrial networks, IEEE 802.3 over optical fiber and IEEE 1901 Broadband Power Line Communications.
  For wireless deployment, consider;
  - Specifications or product descriptions
  - A proper radio planning using appropriate tools
  - Field radio survey to better understand the actual conditions in a given area such as noise and interference
  - Landscape and topology changes in the field such as buildings that may interfere with signal transmission

---
2. Frequency Bands
Frequency bands are ranges of radio wave frequencies used to transmit data in the wireless spectrum, and can further be broken down into WiFi channels. The higher the frequency, the faster the data transmission and shorter the signal range.
- Focusing on IoT access technologies, the frequency bands leveraged by wireless communications are split between licensed and unlicensed bands. Licensed spectrum is generally applicable to IoT long-range access technologies and allocated to communications infrastructures deployed by services providers, public services (for example, first responders, military), broadcasters, and utilities.
  When deploying large numbers of devices in licensed spectrum, there are platforms such as CISCO Jasper Control Center which make automating the provisioning, deployment, and management of large numbers of devices has become much easier.

---
Licensed vs Unlicensed bands
Licensed Spectrum is that in which users must subscribe to services when connecting their IoT devices. Licensed spectrum include
  Cellular, WiMAX and NarrowBand IoT(NB-IoT) Technologies.
Unlicensed means that no guarantees or protections are offered in the ISM(Industrial, Scientific and Medical) bands for device communications. These bands are not regulated
Examples include; 2.4 GHz band as used by IEEE 802.11b/g/n Wi-Fi, IEEE 802.15.1 Bluetooth, IEEE 802.15.4 WPAN
Regulation of bands mandates device compliance on parameters such as transmit power, duty cycle and dwell time, channel bandwidth, and channel hopping.
Unlicensed spectrum is usually simpler to deploy as it does not require service provider but suffer reliability and performance issues frequently than those implementing licensed spectrum
- See … https://www.iotacommunications.com/blog/licensed-vs-unlicensed-spectrum/

---
Sub-GHz range
- Some communications within the ISM bands operate in the sub-GHz range.
  Sub-GHz bands are used by protocols such as IEEE 802.15.4, 802.15.4g, and 802.11ah, and LPWA technologies such as LoRa and Sigfox
  Advantage of Sub-Ghz bands;
  - Sub-GHz bands allow greater distances between devices better than the 2.4 GHz ISM band.
  - Low power consumption
  Disadvantage of Sub-GHz bands;
  - Lower rate of data delivery compared to higher frequencies(not a concern for IoT Sensors)
  Several sub-GHz ranges have been defined in the ISM band. The most well-known ranges are centered on 169 MHz, 433 MHz, 868 MHz, and 915 MHz. However, most IoT access technologies tend to focus on the two sub-GHz frequency regions around 868 MHz and 915 MHz.

---
Band Regulation parameters
- Several bands in different countries are not licensed but they are just regulated.
  The regulators document parameters such as;
  - Channel bandwidth; effective bandwidth multiplied by frequency reuse factor
  - Channel Hopping; works by synchronizing the nodes in the network along a sequence of channels. All nodes must know the sequence and all nodes must know where in the sequence they should be.
  - Transmit Power; The proportionality of effective range to the access point Higher Transmitting power, the farther the signal travel
  - Dwell Time; (or transmit time) is the amount of time needed to transmit on a frequency.
- The UCC in Uganda notes that, the use of wireless devices in the bands 5150-5350 MHz, 5470-5725 MHz and 5725-5825 MHz for Wireless Access Systems including Radio Local Area Networks (WAS/RLAN’s) would be used to enhance wireless connection in the country. For more details https://www.ucc.co.ug/files/downloads/Guidelines-for-use-of-5.8-GHz-ISM-band.pdf

---
3.Power Consumption
A powered node has a direct connection to a power source, and communications are usually not limited by power consumption criteria
- IoT wireless access technologies must address the needs of low power consumption and connectivity for battery-powered nodes.
- This need for reduced power consumption has led to Low-Power Wide-Area (LPWA) wireless environment.
- Wired IoT technologies are not exempted from power consumption

---
4. Topology
A topology defines the way various components communicate with each other within an IoT network.
- Star topology-
- Peer-to-peer-
- Mesh topology-

---
4. Constrained Devices
- While categorizing the class of IoT nodes, constrained devices can be defined in terms of perilous exercise, with computing, memory, storage, power, and networking continuously evolving and improving.
- Constrained nodes have limited resources that impact their networking feature set and capabilities.
  Classes of Constrained Nodes, as Defined by RFC 7228
  Class 0; This class of nodes is severely constrained, with less than 10 KB of memory and less than 100 KB of Flash processing and storage capability forexample a push button.
  Class 1; These nodes can implement an optimized stack specifically designed for constrained nodes, such as Constrained Application Protocol (CoAP) example are environmental sensors.
  Class 2; These nodes are characterized by running full implementations of an IP stack on embedded devices. Example power meter

---
Constrained-Node Networks
These are often referred to as low-power and lossy networks (LLNs).
- Low Power refers to the fact that nodes must cope with the requirements from powered and battery-powered constrained nodes
- Lossy networks indicates that network performance may suffer from interference and variability due to harsh radio environments
  Characteristics of protocols used in constrained-Node Network.
  - Latency and Determinism
  - Data Rate and Throughput
  - Overhead and Payload

---
IoT Access Technologies
- This criteria highlights technologies that are seen as having market and/or mind share.
  The following topics address the IoT access technology
  - Standardization and alliances: The standards bodies that maintain the protocols for a technology
  - Physical layer: The wired or wireless methods and relevant frequencies
  - MAC layer: Considerations at the Media Access Control (MAC) layer, which bridges the physical layer with data link control
  - Topology: The topologies supported by the technology
  - Security: Security aspects of the technology
  - Competitive technologies: Other technologies that are similar and may be suitable alternatives to the given technology

---
Access Technologies
  - IEEE 802.15.4
  - IEEE 802.15.4g and 802.15.4e
  - IEEE 1901.2a
  - IEEE 802.11ah
  - LoRaWAN
  - NB-IoT and Other LTE Variations