Chapter 11
Utilities

---
Introduction
This chapter introduces the concept of the smart grid and explores some of the underlying IoT technologies that are transforming the way power is generated,
transmitted, and delivered. It includes the following sections:
 Introduction to power utility industry
 The GridBlock Reference Model
 The Primary Substation GridBlock and Substation Automation:
 System Control GridBlock:
 The Field Area Network (FAN) GridBlock:
 Securing the Smart Grid:
 The Future of the Smart Grid:

---
An Introduction to the Power Utility Industry
- The three stages of the power supply–chain are generation, transmission, and distribution
  - Generation
  - Transmission
  - Distribution

---
Generation: Power generation is where the electricity gets produced. Power production typically includes nuclear, hydroelectric, gas, and coal pants. Once generated, high-voltage (HV) electrical power is sent through high-voltage transmission lines into the transmission system.
Transmission: Power transmission takes the HV power over long distances—typically 115 kV and above over distances of 50 km and greater. Transmission lines include aerial lines and also submarine cables that transmit HV electrical power over long distances underwater. The transmission system is responsible for connecting HV lines from generation stations to substations throughout the service area.
Distribution: Power distribution includes the part of the utility network from the substation to your home or business. This includes the medium-voltage (12.5 kV, for example) powerlines you see on poles around your neighborhood, including pad mount transformers.

---
The IT/OT Divide in Utilities
While OT networks are not as flexible as their IT counterparts, OT engineering departments have continually adapted to take advantage of newer technologies supporting the power grid.
OT engineers are always looking for better, more cost-effective ways to do things, and this often includes utilizing IT technology whenever possible.
Challenges of concern when IT and OT are interconnected
■ How can network resiliency and redundancy be supported for mission-critical OT applications that keep the lights on?
■ Who will support remote access to distributed systems on the grid that must transit both the IT and OT networks?
■ How will security be governed in both the OT networks and the interconnection points between the IT and OT networks?
■ Will change management be governed in the same way as it is for IT systems, or does the criticality of the OT applications require a new set of rules to ensure the continuity of business?

---
The GridBlocks Reference Model
GridBlocks offers an easy-to-understand model for both novice and advanced users working in the utility space.
The model is forward-looking and is intended to be a generalized end-state reference framework that can help assist in deploying and designing end-to-end secure energy communications solutions for all aspects of the grid, thus facilitating a new and powerful foundation for utilities—the smart grid.
Benefits of GridBlocks reference architecture
■ Details a flexible, tier-based model that supports incremental improvements to logical sections (tiers) of the grid
■ Helps enable secure integration of both new and legacy technologies, improving overall manageability and visibility of network elements
■ Builds on open standards, primarily IP, preventing vendor dependency and also supporting interoperability and thus promoting lower costs
■ Provides a digitization roadmap for utilities, allowing them to modernize different parts of the grid in stages

---
The Primary Substation GridBlock and Substation Automation
There has been not so much progress in Electricity power industry as it is vividly seen in the telecommunication industry, nevertheless, one of the greatest progressive leaps in the past few decades in the electrical power industry has been the ability to connect devices and control them through telecommunications networks, and IoT is now taking this leap to a whole new level.
 SCADA
SCADA is a system by which remote devices can be monitored and controlled by a central server. SCADA plays a critical role in the substation, allowing (as the name suggests) controls and data acquisition from remote devices, known as remote terminal units (RTUs) and intelligent electronic devices (IEDs).

---
The intention of CSADA was to be a system in which an operator could manage remote industrial device	from a central point (often a mainframe computer system).
Over time, remote WAN networks allowed SCADA
connectivity to extend to RTUs, but these connections were typically point-to-point
serial links that utilized RS-232
The legacy substation where the electrical relays are attached via serial (RS-232 or RS-485) connections to RTUs, which are in turn connected to a SCADA gateway device that is connected to the substation Ethernet network.
While we expect these legacy SCADA transport mechanisms to exist for many years to come, long term, traditional SCADA systems are being replaced by a new technology standard that natively takes advantage of Ethernet and TCP/IP: IEC 61850.

---
IEC 61850: The Modernization of Substation Communication Standards
IEC 61850 was built from the ground up on modern standards and technologies and offers a host of new capabilities to IEDs in the substation
The inherent flexibility of Ethernet means that IEDs can easily communicate directly with one another and with other elements of the communications infrastructure.
Another key advantage offered by the flexibility of Ethernet is that interfaces are cheap and are being added by equipment vendors to all modern assets, which means unsupervised gear in the substation is now becoming a thing of the past.

---
- At station level there is communication with SCADA
- Station Bus interconnection between devices in the station level
- Bay level makes connection to power and current transformers.
- Process Bus has a collection of devices that effectively keep an eye on the overall function of their part of the grid.

---
Network Resiliency Protocols in the Substation
These protocols are designed to handle redundancy in the substations which can not be dealt using ITU and REP that are so stringent even to a single packet loss.
This is implemented in two protocols;
 Parallel Redundancy Protocol - PRP is an IEC standard for implementing highly available automation networks which ensures that the network never loses even a single Ethernet frame, even in the event of a network outage.
 High-Availability Seamless Redundancy – Unlike PRP, which relies on parallel network segments, HSR was designed for Ethernet ring topologies. HSR shares many similarities with PRP
One key constraint of HSR is that all intermediary switches in the ring must be capable of understanding HSR to remove the duplicate copy after the primary frame is switched on toward its destination.

---
System Control GridBlock: The Substation WAN
The WAN interconnecting the substations and the control center has become responsible for carrying applications that are intrinsic to the operation of the utility. This includes physical security systems,SCADA, and teleprotection
Protection according to IEC 60384, is defined as “the provision for detecting faults or other abnormal conditions in a power system, for enabling fault clearance, for terminating abnormal conditions, and for initiating signals or indications.”
Teleprotection is the mechanism by which this information is transported over a network.
There are two common types of protection: distance protection and current differential line protection. Whatever the protection scheme, a communication system is always required between the relays

---
Distance Protection
Distance protection monitors unacceptable variations in circuit impedance over a predetermined distance. If a relay sees a change in the impedance beyond acceptable thresholds, the relay determines that there is a fault on the line.
For a known line distance, the relay
simply needs to measure the impedance of the line at key points, and then a calculation can show where the break is.
If the measured impedance is different from what is expected, the relay can signal to the switch to either enable or disable a feeder line.
The relays measure impedance in the different zones and use this to isolate the location ofthe fault.

---
Current Differential (87L) Protection
Unlike distance protection, current differential protection compares current samples between two distant relays in different substations. For example, a nonzero differential in the current implies that there is a fault somewhere on the line that will cause the relays to trip.
For AC, timing is required for sync
between the substations otherwise
a false relay signal indicating power outage.
GPS-Sync is used to sync relays so that current
 is aligned, channeled based sync is also used to exchange timestamped messages between relays

---
Designing a WAN for Teleprotection
most modern utilities are now migrating to multipurpose packet networks such as MPLS to transport nearly all their applications, including teleprotection.
 They are flexible, easy to scale, multitenant, and multiservice;
 They are able to carry a host of different applications; and
 They can even transport legacy protocols through channel emulation and tunneling services.
The downside of the IP-based WANS is that they don’t have support for predictable path with latency.
MPLS–Transport Profile (MPLS-TP), which brings capabilities for traffic engineering, automatic protection switching (APS), and Operations, Administration and Management

---
MPLS-TP transports a point-to-point pseudo-wire (a virtual circuit transported over MPLS) over a prescriptive label switch path (LSP).
Hop-by-hop LSP makes latency predictable and symmetrical,
and it also keeps jitter to a minimum
MPLS-TP also supports APS by identifying a known backup LPS path in case of a primary LSP failure.
MPLS-TP is that it supports end-to-end OAM. OAM allows for fault detection of the pseudo-wire at any point and is used as the trigger mechanism to fail over to a backup LSP.
MPLS-TP implements in-band OAM capabilities using a generic associated channel (G-ACh) based on RFC 5085 (Virtual Circuit Connectivity
Verification [VCCV])

---
The Field Area Network (FAN) GridBlock