Application Protocols for IoT
In this chapter we look at the following;
The Transport Layer:
IP-based networks use either TCP or UDP. However, the constrained nature of IoT	networks requires a closer look at the use of these traditional transport mechanisms.
IoT Application Transport Methods:
This section explores the various types of IoT application data and the ways this data can	be carried across a network.

---
The Transport Layer
Protocols specified for the transport layer
1.Transmission Control Protocol (TCP):
  This connection-oriented protocol requires a session to get established between the source and destination before exchanging
  data
- 2. User Datagram Protocol (UDP):
  This is a connection-less protocol, data can be quickly sent between source and destination—but with no guarantee of delivery

---
Reasons why TCP is preferred to UDP
- TCP is the main protocol used at the transport layer. This is largely due to its inherent characteristics, such as its ability to transport large volumes of data into smaller sets of packets.
- It ensures reassembly in a correct sequence, flow control and window adjustment, and retransmission of lost packets
  UDP is used in the following protocols;
  - Domain Name System (DNS),
  - Network Time Protocol (NTP),
  - Simple Network ManagementProtocol (SNMP)
  - Dynamic Host Control Protocol (DHCP)

---
IoT Application Transport Methods