Application Protocols for IoT
In this chapter we look at the following;
The Transport Layer:
IP-based networks use either TCP or UDP. However, the constrained nature of IoT	networks requires a closer look at the use of these traditional transport mechanisms.
IoT Application Transport Methods:
This section explores the various types of IoT application data and the ways this data can	be carried across a network.

---
The Transport Layer
Protocols specified for the transport layer
1.Transmission Control Protocol (TCP):
  This connection-oriented protocol requires a session to get established between the source and destination before exchanging
  data
- 2. User Datagram Protocol (UDP):
  This is a connection-less protocol, data can be quickly sent between source and destination—but with no guarantee of delivery

---
Reasons why TCP is preferred to UDP
- TCP is the main protocol used at the transport layer. This is largely due to its inherent characteristics, such as its ability to transport large volumes of data into smaller sets of packets.
- It ensures reassembly in a correct sequence, flow control and window adjustment, and retransmission of lost packets
  UDP is used in the following protocols;
  - Domain Name System (DNS),
  - Network Time Protocol (NTP),
  - Simple Network ManagementProtocol (SNMP)
  - Dynamic Host Control Protocol (DHCP)

---
IoT Application Transport Methods
- The following categories of IoT application protocols and their transport methods
  - Application layer protocol not present:
  - Supervisory control and data acquisition (SCADA)
  - Generic web-based protocols:
  - IoT application layer protocols:

---
Application Layer Protocol Not Present
Data broker is piece of middleware that standardizes sensor output into a common format that can then be retrieved by authorized applications.
- An IoT data broker is needed to scale this method of transporting application data.

---
SCADA
SCADA is an automation control system that was initially implemented without IP over serial links, before being adapted to Ethernet and IPv4.

---
Adapting SCADA for IP
This technique utilizes an IP adaptation layer to transport application data that comes from a non-IP stack
- DNP3 (adopted by IEEE 1815-2012) specifies the use of TCP or UDP on port
20000 for transporting DNP3 messages over IP.
- The Modbus messaging service utilizes TCP port 502.
- IEC 60870-5-104 is the evolution of IEC 60870-5-101 serial for running over
Ethernet and IPv4 using port 2404.
- DLMS User Association specified a communication profile based on TCP/IP in the DLMS/COSEM Green Book (Edition 5 or higher), or in the IEC 62056-53 and IEC62056-47 standards, allowing data exchange via IP and port 4059.