Application Protocols for IoT
This chapter focuses on the transport of application protocols in IoT networks;
The Transport Layer:
IP-based networks use either TCP or UDP. However, the constrained nature of IoT	networks requires a closer look at the use of these traditional transport mechanisms.
IoT Application Transport Methods:
This section explores the various types of IoT application data and the ways this data can	be carried across a network.

---
The Transport Layer
Protocols specified for the transport layer include the following;
1.Transmission Control Protocol (TCP):
  This connection-oriented protocol requires a session to get established between the source and destination before exchanging
  data
- 2. User Datagram Protocol (UDP):
  This is a connection-less protocol, data can be quickly sent between source and destination—but with no guarantee of delivery

---
Reasons why TCP is preferred to UDP
- TCP is the main protocol used at the transport layer. This is largely due to its inherent characteristics, such as its ability to transport large volumes of data into smaller sets of packets.
- It ensures reassembly in a correct sequence, flow control and window adjustment, and retransmission of lost packets
  UDP is used in the following protocols;
  - Domain Name System (DNS),
  - Network Time Protocol (NTP),
  - Simple Network ManagementProtocol (SNMP)
  - Dynamic Host Control Protocol (DHCP)

---
IoT Application Transport Methods
Because of the diverse types of IoT application protocols, there are various means for transporting these protocols across a network.
To deal with legacy utility and industrial IoT protocols that have certain requirements, while other
times you might need to consider the transport requirements of more modern application layer protocols.
The following categories of IoT application protocols and their transport methods
  - Application layer protocol not present:
  - Supervisory control and data acquisition (SCADA)
  - Generic web-based protocols:
  - IoT application layer protocols:

---
Method 1: Application Layer Protocol Not Present
- In this method, data payload is directly transported on top of the lower layers. An IoT data broker is needed to scale this method of transporting application data
- IoT devices are usually simple smart objects that are severely constrained. Implementing a robust protocol stack is usually not useful and sometimes not even possible with the limited available resources.
- Data broker is piece of middleware that standardizes sensor output into a common format that can then be retrieved by authorized applications.
- An IoT data broker is needed to scale this method of transporting application data.

---
Method 2: IP-adapted application layer
This technique utilizes an IP adaptation layer to transport application data that comes from a non-IP stack.
Legacy industrial protocols, such as DNP3, fall in this category and require capabilities like raw sockets and protocol translation to successfully communicate across an IP network.

---
SCADA
- The evolution of older protocols that connected sensors and actuators have adapted themselves to utilize IP and this evolution is known as Supervisory Control And Data Acquisition (SCADA)
- SCADA is an automation control system that was initially implemented without IP over serial links, before being adapted to Ethernet and IPv4.
  Adapting SCADA for IP
  - To have the ability to leverage existing equipment and standards while integrating seamlessly the SCADA subnetworks to the corporate WAN infrastructures.
  - Assigning TCP/UDP port numbers to the protocols such as
    - DNP3 (adopted by IEEE 1815-2012) specifies the use of TCP or UDP on port 20000
    - The Modbus messaging service utilizes TCP port 502.
    - IEC 60870-5-104 on port 2404.
    - DLMS User Association specified a communication profile based on TCP/IP

---
Tunneling Legacy SCADA over IP Networks
Transport of the original serial protocol over IP can be achieved either by tunneling using raw sockets over TCP or UDP or by installing an intermediate device that performs protocol translation between the serial protocol version and its IP implementation

---
SCADA Protocol Translation
With protocol translation, the legacy serial protocol is translated to a corresponding IP version.
The IoT gateway in this figure below performs a protocol translation function that enables communication between the RTUs and servers, despite the fact that a serial connection is present on one side and an IP connection is used on the other.This can be accomplished by offering computing resources on IoT gateways or routers.

---
SCADA Transport over LLNs with MAP-T
Most of the industrial devices supporting IP today support IPv4 only. When deployed over LLN subnetworks that are IPv6 only, a transition mechanism, such as MAP-T (Mapping of Address and Port using Translation) needs to be implemented.
This allows the deployment to take advantage of native IPv6 transport transparently to the application and devices.
MAP-T makes the appropriate mappings between IPv4 and the IPv6 protocols. This allows legacy IPv4 traffic to be forwarded across IPv6 networks.
In other words, older devices and protocols can continue running IPv4 even though the network is requiring IPv6.

---
Method 3: Generic Web-Based Protocols
The Internet of Things greatly benefits from the existing web-based protocols. These protocols, including HTTP/HTTPS and XMPP, ease the integration of IoT devices in the Internet world through well-known and scalable programming techniques.
However, to fully address constrained devices and networks, optimized IoT protocols are required.

---
Method 4: IoT application layer protocols
- These are lightweight protocols that are better suited to large numbers of constrained nodes and networks.
- Two of the most popular protocols are ;
  - CoAP
  - MQTT.

---
CoAP
- Constrained Application Protocol is a generic framework for
  resource-oriented applications targeting constrained nodes and networks
- The CoAP framework defines simple and flexible ways to manipulate sensors and actuators for data or device management.
  The IETF CoRE working group has published multiple standards-track specifications for CoAP, including the following:
  - RFC 6690: Constrained RESTful Environments (CoRE) Link Format.
  - RFC 7252: The Constrained Application Protocol (CoAP)
  - RFC 7641: Observing Resources in the Constrained Application Protocol (CoAP)
  - RFC 7959: Block-Wise Transfers in the Constrained Application Protocol (CoAP)
  - RFC 8075: Guidelines for Mapping Implementations: HTTP to the Constrained
  - Application Protocol (CoAP)

---
The CoAP messaging model is primarily designed to facilitate the exchange of messages
over UDP between endpoints, including the secure transport protocol Datagram Transport Layer Security (DTLS).

---
CoAP communications across an IoT infrastructure can take various paths.
Connections can be between devices located on the same or different constrained networks or between devices and generic Internet or cloud servers, all operating over IP.

---
- Just like HTTP, CoAP is based on the REST architecture, but with a “thing” acting as
  both the client and the server.
- Through the exchange of asynchronous messages, a client requests an action via a method code on a server resource.
- A uniform resource identifier(URI) localized on the server identifies this resource. The server responds with a response code that may include a resource representation. The CoAP request/response semantics
  include the methods GET, POST, PUT, and DELETE.

---
CoAP defines four types of messages: confirmable, non-confirmable, acknowledgement, and reset in a message response or a request
While running over UDP, CoAP offers a reliable transmission of messages when a CoAP
header is marked as “confirmable.”
CoAP supports basic congestion control with a default time-out, simple stop and wait retransmission with exponential back-off mechanism, and detection of duplicate messages through a message ID.

---
- Much as with accessing web server resources, CoAP specifications provide a description of the relationships between resources in RFC 6690, “Constrained RESTful Environments (CoRE) Link Format.”
  This standard defines the CoRE Link format carried as a payload with an assigned Internet media type.
  To improve the response time and reduce bandwidth consumption, CoAP supports caching capabilities based on the response code.
- CoAP is fully optimized for IoT constrained nodes and networks, while leveraging traditional web programming techniques to make it easily understandable by the development community

---
Message Queuing Telemetry Transport (MQTT)
Is an extremely simple protocol with only a few options designed with considerations for constrained nodes, unreliable WAN backhaul communications, and bandwidth constraints with variable latencies.

---
- An MQTT client can act as a publisher to send data (or resource information) to an MQTT server acting as an MQTT message broker.
- The MQTT server (or message broker) accepts the network connection along with application messages, such as Temp/RH data, from the publishers.
- With MQTT, clients can subscribe to all data (using a wildcard character) or specific data from the information tree of a publisher.
- The presence of a message broker in MQTT decouples the data transmission between clients acting as publishers and subscribers.
- A benefit of having this decoupling is that the MQTT message broker ensures that information can be buffered and cached in case of network failures.
- MQTT control packets run over a TCP transport using port 1883. TCP ensures an ordered, lossless stream of bytes between the MQTT client and the MQTT server.

---
- MQTT is a lightweight protocol because each control packet consists of a 2-byte fixed header with optional variable header fields and optional payload.
- Note that a control packet can contain a payload up to 256 MB. Figure 6-11 provides an overview of the MQTT message format.
- Compared to the CoAP message format, MQTT contains a smaller header of 2 bytes compared to 4 bytes for CoAP.

---
MQTT is different from the “one-to-one” CoAP model in its “many-to-many” subscription framework, which can make it a better option for some deployments.
MQTT is TCP-based, and it ensures an ordered and lossless connection. It has a low overhead when optionally paired with UDP and flexible message format, supports TLS for security, and provides for three levels of QoS.