Application Protocols for IoT
In this chapter we look at the following;
The Transport Layer:
IP-based networks use either TCP or UDP. However, the constrained nature of IoT	networks requires a closer look at the use of these traditional transport mechanisms.
IoT Application Transport Methods:
This section explores the various types of IoT application data and the ways this data can	be carried across a network.

---
The Transport Layer
Protocols specified for the transport layer
1.Transmission Control Protocol (TCP):
  This connection-oriented protocol requires a session to get established between the source and destination before exchanging
  data
- 2. User Datagram Protocol (UDP):
  This is a connection-less protocol, data can be quickly sent between source and destination—but with no guarantee of delivery

---
Reasons why TCP is preferred to UDP
- TCP is the main protocol used at the transport layer. This is largely due to its inherent characteristics, such as its ability to transport large volumes of data into smaller sets of packets.
- It ensures reassembly in a correct sequence, flow control and window adjustment, and retransmission of lost packets
  UDP is used in the following protocols;
  - Domain Name System (DNS),
  - Network Time Protocol (NTP),
  - Simple Network ManagementProtocol (SNMP)
  - Dynamic Host Control Protocol (DHCP)

---
IoT Application Transport Methods
- The following categories of IoT application protocols and their transport methods
  - Application layer protocol not present:
  - Supervisory control and data acquisition (SCADA)
  - Generic web-based protocols:
  - IoT application layer protocols:

---
Application Layer Protocol Not Present
IoT devices are usually simple smart objects that are severely constrained. Implementing a robust protocol stack is usually not useful and sometimes not even possible with the limited available resources.
- Data broker is piece of middleware that standardizes sensor output into a common format that can then be retrieved by authorized applications.
- An IoT data broker is needed to scale this method of transporting application data.

---
SCADA
- The evolution of older protocols that connected sensors and actuators have adapted themselves to utilize IP and this evolution is known as Supervisory Control And Data Acquisition (SCADA)
- SCADA is an automation control system that was initially implemented without IP over serial links, before being adapted to Ethernet and IPv4.
  Adapting SCADA for IP
  - To have the ability to leverage existing equipment and standards while integrating seamlessly the SCADA subnetworks to the corporate WAN infrastructures.
  - Assigning TCP/UDP port numbers to the protocols such as
    - DNP3 (adopted by IEEE 1815-2012) specifies the use of TCP or UDP on port 20000
    - The Modbus messaging service utilizes TCP port 502.
    - IEC 60870-5-104 on port 2404.
    - DLMS User Association specified a communication profile based on TCP/IP

---
Tunneling Legacy SCADA over IP Networks
Transport of the original serial protocol over IP can be achieved either by tunneling using raw sockets over TCP or UDP or by installing an intermediate device that performs protocol translation between the serial protocol version and its IP implementation

---
SCADA Protocol Translation
With protocol translation, the legacy serial protocol is translated to a corresponding IP version.
- The IoT gateway in this figure below performs a protocol translation function that enables communication between the RTUs and servers, despite the fact that a serial connection is present on one side and an IP connection is used on the other.
- This can be accomplished by offering computing resources on IoT gateways or routers, as shown in this protocol translation example